Maypole L35 Fog-lamps for Midas Bronze (later bumper)

Cost £10.95 from www.towsure.co.uk

Diameter:

- 145mm (fits perfectly!)

Construction:

- Plastic and zinc plated hardware so no rust tears. Shallow construction so no need to cut body (except a single drill hole for mounting bolt – referred later as “bolt 2”)

Fitting Instructions:

Note: There is a squared off "U" shaped mounting bracket, supplied with each lamp, which has 2 holes at the tips of the "U" ("bolt 1" goes though these and the lamp bowl and is the pivot for up/down adjustment of the lamp) and another hole at the flat base of the “U” ("bolt 2" goes through this and the Midas's body – these will come through the body near the sides of radiator under the bonnet)

Fog Lamp Grill Removal

Note: This is not essential but the lamp grills are pretty ungainly. They are moulded into the retaining ring but can be removed as follows:

- Cut each leg of the grill close to the lamp retaining ring (a Dremmel with cutting disk is excellent)

- Sand down each stump. A Dremmel with roll sanding disk works very well and leaves surface looking good – you will need to carefully sand down then carefully “oversand” the ring either side. It sounds more difficult than it is but the results are worth is as the plain ring without grill looks much more professional. Wire wool will finish it off.

Mounting:

- Attach “U” shaped mounting bracket to bowl using pivot bolt 1.

- Adjust bracket to make the flat surface at the base of the "U" parallel with the lamp (note: the angle at which the lamp will eventually sit is the same angle approx of the bodywork on which you will be mounting the lamp)

- To work out where to drill the body for bolt 2, screw the bolt through the bracket hole with nut 2 on the bowl side (ie the wrong way round).

- Put a drop of oil on the bolt head and carefully offer up the lamps tilted at an angle to match the bumper. As the lamp fits the bumper so well, this will give a perfect mark for drilling. Remove nut and bolt 2

- Drill a pilot through the centre of the mark then enlarge with several larger drills to prevent tearing of the GRP

- Push bolt 2 through from the lamp bowl side (ie. the correct way round) and tape it to the bracket to hold in place (this will save lots of frustration later!), use large washers (equivalent to the depth of the bolt head used to mark earlier) between bracket and body for spacing,

- Offer up lamp pushing bolt 2 through body

- Under the bonnet, put a large washer and lock washer over the bolt end, then screw on nut to finish.

I have not given wiring instructions as these are pretty standard for Fog and Spot lamps.