Midas Clutch Pedal Modification

I've just followed the advice mentioned regarding the modifying the position of the clutch pedal as my clutch biting point was very close to the floor making for quite a pain in traffic. In the end, the route I took was to slightly move the clutch master cylinder clevis pin location hole on the top part of the clutch pedal – the process was as follows:

Take off the clutch pedal (remove the master cylinder clevis pin then brake/clutch pivot bolt), then, with the pedal placed on a sheet of cardboard on its side, draw around the pedal and the clevis pin hole (with pencil) to record the original profile (similar to picture below).

Use a grinder with cutting disk to almost cut through the pedal between the main pivot hole and the clevis pin hole to about 1/4" from the edge (see picture)

Using a vice, bend the section containing the clevis pin hole upwards until the new base of the clevis pin hole is in the position that had been the position of the top of the clevis pin hole previously when you compare with the template (this will make the cut open out to a V shape).

Weld up the cut, grind the weld smooth, prime and paint (if done soon after welding the paint will dry quickly as the metal is warm), then refit.

This took just over an hour to do from start to finish and has transformed the way the car drives.

# Text boxes

Clevis Pin Hole

Cut Made Here

Bend Up after cutting

Pivot Hole